Test Box Setup Procedure

SCRIPT FOR COMPILING SOURCE DEPENING ON (detect) OS/32/64bit, etc

Software To Have Installed:
git, Dropbox, Xilinx ISE Design (Webpack, free, to be used), LPCXpresso (Free Edition), openJDK 7 jre/jdk.
Extra: cmake, ROS (for /addons, /config)

Procedure:

1: Clone the following repositories:
git@git.assembla.com:oip_scm.git
git@git.assembla.com:saferemotecontrol.git
https://github.com/humanisticrobotics/hri-safe-remote-control-system

2: Run the makefiles in the following directories: (make clean is suggested)
firmware/lpc21isp
drivers/C: make sure /lib exists (mkdir lib)
drivers/analyzer: extract tar first.

Notes:
1. Test Box was a DELL Dimension c521 with AMD64 running Ubuntu 12.04 LTS (32-Bit)
2. Make clean should be run to ensure object files are compatible for test system. (Compiled for 32/64Bit).
3. /tools contains the Java GUI for the downloader/config of SRC, scripts to program LP1768.
4. /sandbox contains some demo, ROS software.
5. ./hri_safety_sense and _test use ROS.