VSC Assembly Procedure Humanistic Robotics, Inc.

PO Number:	_______________________________________________
Serial Number:	_______________________________________________

Step	Notes / Versions	Operator Initial
Perform required VSC board mods
Mount radio to VSC Board
Program CPLD Version using ISE Impact
Program uC Bootloader using JTAG
Program uC Setup Firmware using bootloader / USB
Use setup program to write Configurations
- Serial Number
- Radio Network ID
- Radio Power Level
- Wireless SW Configuration
- Wired SW Configuration
- CAN Bus Speed (if applicable)
Program uC Application Firmware using bootloader
Assemble top of VSC w/ correct cabling
Assemble bottom of VSC w/ VSC board
Assemble top/bottom of VSC into final product
Perform qualification tests on assembled unit
Perform final inspection

Notes: